[sudo] password for hwp:

Welcome to minicom 2.7

OPTIONS: I18n
Compiled on Jan 1 2014, 17:13:22.
Port /dev/ttyUSB2, 10:20:14

Press CTRL-A Z for help on special keys

nessos>
nessos>enable
Password:
nessos#conf t
Enter configuration commands, one per line. End with CNTL/Z.
nessos(config)#interface FastEthernet0/1/0
nessos(config-if)#no shutdown
nessos(config-if)#exit
nessos(config)#interface FastEthernet0/1/0.21
nessos(config-subif)#encapsulation dot1Q 21
nessos(config-subif)#ip address 10.2.1.254 255.255.255.0
nessos(config-subif)#exit
nessos(config)#interface FastEthernet0/1/0.22
nessos(config-subif)#encapsulation dot1Q 22
nessos(config-subif)#ip address 10.2.2.254 255.255.255.0
nessos(config-subif)#exit
nessos(config)#interface GigabitEthernet0/0
nessos(config-if)#ip address 10.3.2.1 255.255.255.0
nessos(config-if)#no shutdown
nessos(config-if)#exit
nessos(config)#interface FastEthernet0/2/0
nessos(config-if)#ip address 10.3.5.1 255.255.255.0
nessos(config-if)#no shutdown
nessos(config-if)#exit
nessos(config)#ip route 10.1.1.0 255.255.255.0 10.3.2.2
nessos(config)#ip route 10.1.2.0 255.255.255.0 10.3.5.2
nessos(config)#exit
nessos#show ip route
Codes: C - connected, S - static, R - RIP, M - mobile, B - BGP
       D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
       N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2
       E1 - OSPF external type 1, E2 - OSPF external type 2
       i - IS-IS, su - IS-IS summary, L1 - IS-IS level-1, L2 - IS-IS level-2
       ia - IS-IS inter area, * - candidate default, U - per-user static route
       o - ODR, P - periodic downloaded static route

Gateway of last resort is not set

     172.16.0.0/24 is subnetted, 1 subnets
C 172.16.32.0 is directly connected, GigabitEthernet0/1
     10.0.0.0/24 is subnetted, 6 subnets
C 10.2.1.0 is directly connected, FastEthernet0/1/0.21
S 10.1.2.0 [1/0] via 10.3.5.2
C 10.2.2.0 is directly connected, FastEthernet0/1/0.22
S 10.1.1.0 [1/0] via 10.3.2.2
C 10.3.2.0 is directly connected, GigabitEthernet0/0
C 10.3.5.0 is directly connected, FastEthernet0/2/0
S 132.187.0.0/16 [1/0] via 172.16.32.1
nessos#

[sudo] password for hwp:

Welcome to minicom 2.7

OPTIONS: I18n
Compiled on Jan 1 2014, 17:13:22.
Port /dev/ttyUSB0, 10:03:28

Press CTRL-A Z for help on special keys

ate>enable
Password:
ate#conf t
Enter configuration commands, one per line. End with CNTL/Z.
ate(config)#interface GigabitEthernet 0/1
ate(config-if)#ip address 10.3.1.2 255.255.255.0
ate(config-if)#no shutdown
ate(config-if)#exit
ate(config)#interface GigabitEthernet 0/0
ate(config-if)#ip address 10.3.2.2 255.255.255.0
ate(config-if)#no shutdown
ate(config-if)#exit
ate(config)#ip route 10.1.1.0 255.255.255.0 10.3.1.1
ate(config)#ip route 10.2.1.0 255.255.255.0 10.3.2.1
ate(config)# exit

ate#show ip route
Codes: C - connected, S - static, R - RIP, M - mobile, B - BGP
       D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
       N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2
       E1 - OSPF external type 1, E2 - OSPF external type 2
       i - IS-IS, su - IS-IS summary, L1 - IS-IS level-1, L2 - IS-IS level-2
       ia - IS-IS inter area, * - candidate default, U - per-user static route
       o - ODR, P - periodic downloaded static route

Gateway of last resort is not set

     10.0.0.0/24 is subnetted, 4 subnets
C 10.3.1.0 is directly connected, GigabitEthernet0/1
S 10.2.1.0 [1/0] via 10.3.2.1
S 10.1.1.0 [1/0] via 10.3.1.1
C 10.3.2.0 is directly connected, GigabitEthernet0/0

[sudo] password for hwp:

Welcome to minicom 2.7

OPTIONS: I18n
Compiled on Jan 1 2014, 17:13:22.
Port /dev/ttyUSB1, 10:38:08

Press CTRL-A Z for help on special keys

styx>enable
Password:
styx#conf t
Enter configuration commands, one per line. End with CNTL/Z.
styx(config)#interface FastEthernet0/1/0
styx(config-if)#no shutdown
styx(config-if)#exit
styx(config)#interface FastEthernet0/1/0.11
styx(config-subif)#encapsulation dot1Q 11
styx(config-subif)#ip address 10.1.1.254 255.255.255.0
styx(config-subif)#exit
styx(config)#interface FastEthernet0/1/0.12
styx(config-subif)#encapsulation dot1Q 12
styx(config-subif)#ip address 10.1.2.254 255.255.255.0
styx(config-subif)#exit
styx(config)#interface GigabitEthernet0/1
styx(config-if)#ip address 10.3.1.1 255.255.255.0
styx(config-if)#no shutdown
styx(config-if)#exit
styx(config)#interface FastEthernet0/2/0
styx(config-if)#ip address 10.3.4.1 255.255.255.0
styx(config-if)#no shutdown
styx(config-if)#exit
styx(config)#ip route 10.2.1.0 255.255.255.0 10.3.1.2
styx(config)#ip route 10.2.2.0 255.255.255.0 10.3.4.2
styx(config)# exit
styx>show ip route
Codes: C - connected, S - static, R - RIP, M - mobile, B - BGP
       D - EIGRP, EX - EIGRP external, O - OSPF, IA - OSPF inter area
       N1 - OSPF NSSA external type 1, N2 - OSPF NSSA external type 2
       E1 - OSPF external type 1, E2 - OSPF external type 2
       i - IS-IS, su - IS-IS summary, L1 - IS-IS level-1, L2 - IS-IS level-2
       ia - IS-IS inter area, * - candidate default, U - per-user static route
       o - ODR, P - periodic downloaded static route

Gateway of last resort is not set

     172.16.0.0/24 is subnetted, 1 subnets
C 172.16.32.0 is directly connected, GigabitEthernet0/0
     10.0.0.0/24 is subnetted, 6 subnets
C 10.3.1.0 is directly connected, GigabitEthernet0/1
S 10.2.1.0 [1/0] via 10.3.1.2
C 10.1.2.0 is directly connected, FastEthernet0/1/0.12
S 10.2.2.0 [1/0] via 10.3.4.2
C 10.1.1.0 is directly connected, FastEthernet0/1/0.11
C 10.3.4.0 is directly connected, FastEthernet0/2/0
S 132.187.0.0/16 [1/0] via 172.16.32.1